## Slide 1
H. Brunner Review of ICD Oct. 25th, 2018
eROSITA mission planning and operations:
IKI/MPE interactions
(review of SRG Science Ground Segment IKI/MPE ICD)
Transfer of SRG data from IKI to MPE
Transfer of mission planning information
between IKI and MPE
Interactions during ground contacts
Changes of a scheduled observing timeline
Appendices:
  SRG operational parameters
  Data formats
  eROSITA command interface
  Data exchange FTP server
  Contact information
1/10

## Slide 2
H. Brunner Review of ICD Oct. 25th, 2018
Transfer of SRG data from IKI to MPE
    3.1.4 eROSITA data embedded in the engineering data
eROSITA data embedded in the spacecraft engineering data are made available to MPE. The data are transmitted to MPE immediately after reception at IKI (appendix 3).
3.1.5 Auxiliary datasets (Types of data)
Reaction wheel unloading times
The start and end times of the time periods when the reaction wheels were unloaded will be provided. Preliminary reaction wheel unloading times are also made available as part of the mission planning activities (see section 4).
ART-XC background light curves
The eROSITA calibration team at MPE has expressed interest to receive ART-XC background lightcurves for eROSITA calibration purposes. This was approved by the Russian side. Technical details are under discussion.
2/10

## Slide 3
H. Brunner Review of ICD Oct. 25th, 2018
Transfer of SRG data from IKI to MPE
3.2.4 Auxiliary datasets (Data formats)
Time synchronization files and clock reset times
Clock reset times will be provided as part of the SRG engineering data, made available to MPE (see appendix 3 for details). The data format of the time synchronization files is described in appendix 2.
Reaction wheel unloading times
These will be provided as part of the SRG engineering data (see appendix 3 for details).
3.3.1 IKI to MPE socket connection
3.3.2 IKI to MPE file based data transfer
Now in progress!
3/10

## Slide 4
H. Brunner Review of ICD Oct. 25th, 2018
Transfer of mission planning information between IKI and MPE
Approval of planning files
The MPE/Hamburg mission planning files are reviewed and approved by the mission planning team points of contact, SRG operations team, the science instrument teams and the eROSITA and ART-XC project scientists and instrument PIs. If a planning file is not approved, modifications are proposed to the Hamburg mission planning team and a new version is created and reviewed.
Processing of the planning files
After approval the MPE/Hamburg mission planning files are processed at IKI. This process is repeated each time a revised version of the planning file is created.
The IKI mission planning team will translate the MPE/Hamburg mission planning files into the NPOL/IKI monthly planning file format (described in appendix 5). The observation IDs (obsIDs) and observation interval numbers (OBIs) will be copied over from the MPE/Hamburg mission planning files to the NPOL/IKI monthly planning files. The NPOL/IKI monthly planning files will be stored in the data exchange FTP server at IKI, where they will be available to the MPE/Hamburg mission planning team for verification (the folder structure of the data exchange FTP server at IKI is described in appendix 8). NPOL will subsequently access the NPOL/IKI monthly planning files for further processing and execution.
4/10

## Slide 5
H. Brunner Review of ICD Oct. 25th, 2018
Transfer of mission planning information between IKI and MPE
In addition, the eROSITA instrument team will translate the part of the MPE/Hamburg mission planning files specifying the eROSITA observing modes into sequences of suspended commands and copy them to the appropriate directory of the data exchange FTP server at IKI. IKI personnel will combine the eROSITA commands with ART-XC commands (if any) and copy them to the outgoing folder for further processing and execution by NPOL (also see section 5.1.1).
4.1.6 Times of scheduled reaction wheel unloading
5/10

## Slide 6
H. Brunner Review of ICD Oct. 25th, 2018
Transfer of mission planning information between IKI and MPE
4.2.1 MPE/Hamburg mission planning files (Data formats)
The data format is described in appendix 6.
Add (some) scan observing mode parameters (Z_SCAN, Y_STEP, SPEED, N_PASS)
For all sky survey operations: use same angles as in NPOL/IKI monthly planning files to avoid conversion errors?
Questions to science teams:
Size and location of IKI PV field? Did we agree on the all-sky survey scanning law for the first 6 month survey?
4.3.1 MPE/Hambug mission planning files (Method of data transfer)
The MPE/Hamburg mission planning files are uploaded to the data exchange FTP site at IKI (appendix 8 and 9). Any update of the planning files in this area is announced by emails to the mission planning points of contact. In addition, each side acknowledges to the mission planning points of contact when the updated planning files were received and/or processed.
6/10

## Slide 7
H. Brunner Review of ICD Oct. 25th, 2018
Interaction during ground contacts
5.1.1 Procedures and timescales for sending eROSTA telecommand sequences
Needs update:
on-demand commands supplied ahead of a groud contact are ‘released‘ by referring to their asterix number.
eROSITA will be able to refer to commands via their database command instance number by accessing the seance session plan XML file on the data exchange server .
ACT01-2018-09-07 of ground segment progress meeting:
PG will provide an example seance session plan file containing eROSITA
commands. MPE will provide feedback whether the format is sufficiently
human-readble or whether some post-processing is required.
How do we know from Munich when a specifi command was executed?
ACT02-2018-09-07 of ground segment progress meeting:
PG will explore options how the exact times of command issuance can be
comunicated to MPE. DC will verify how eROSITA command execution can be
accessed in the eROSITA telemetry.
7/10

## Slide 8
H. Brunner Review of ICD Oct. 25th, 2018
Interaction during ground contacts
5.3 Interactions while the MPE team is on site at IKI during the inital mission phase
The MPE eROSITA team will stay at IKI for a tbd time period after launch. A copy of the eROSITA EGSE located at IKI and operated by MPE experts will receive eROSITA data (as described in chapter 3.3.1 ‘IKI to MPE socket connection’) .
5.4. Interactions between MPE and II during later mission phases
… The eROSITA EGSE at IKI (section 5.3) will remain at IKI and can be used by IKI personnel acting in close coordination with MPE experts. IKI and MPE experts will interact via video conference link and as needed via other channels (phone, email, file transfer) during ground contacts. In the absence or unavailability of MPE personnel, IKI personnel may issue routine eROSITA commands, such as for initiating a routine data dump.
8/10

## Slide 9
H. Brunner Review of ICD Oct. 25th, 2018
Changes of a scheduled observing timeline (tbc)
6.1.1 Scheduled changes for technical reasons
The SRG operations team and the science instrument teams can request to modify an already scheduled observing timeline for important technical reasons by informing the mission planning, science instrument, and SRG operations points of contact … .
6.1.2 Scheduled changes for science reasons (ToOs)
The instrument PIs can jointly request changes of the scheduled observing timeline.
The same procedures and timescales as described in section 6.1.1 apply.
6.2.1 Last minute changes for technical reasons
Last minute changes or interruptions of a scheduled observing timeline, including
SRG save-mode commanding, can be implemented by the SRG operations team
for urgent mission critical reasons. …
In the absence or unavailability of the eROSITA instrument team, eROSITA
safe-mode commanding may be conducted by the SRG operations team in clearly
defined emergency situations (details tbd).
6.2.2 Last minute changes for science reaons (ToO)
The instrument PIs can jointly request last minute changes of a scheduled observing timeline by informing the project scientists, instrument teams, mission planning team and SRG operations team. …
9/10

## Slide 10
H. Brunner Review of ICD Oct. 25th, 2018
Contact information
Principal investigators
Project scientists
Instrument teams (PoC)
Calibration teams (PoC)
Mission planning (IKI/LA/MPE/Hamburg PoC)
SRG operations (PoC)
Field scanning mode
Damping time at start of scan: 100s
Damping time at end of scan: 80s
Damping time for transfer to next scan: 5s
Appendix 1: SRG operational parameters
10/10